Interface Definition for Base Movements

# Input Summary
Base controller subscribes to the following topics:
- /base_cntrl/go_back
- /base_cntrl/go_fwd
- /base_cntrl/go_left
- /base_cntrl/go_right
- /base_cntrl/go_to_pose
- /base_cntrl/scout_to_pose
- /base_cntrl/in_cmd
- /base_cntrl/rotate_deg
- /base_cntrl/path_cost_qry

# Output Summary
Base controller publishes the following topics:
- /base_cntrl/path_cost
- /base_cntrl/out_result
- /base_cntrl/cost_list

# Input Description
## /base_cntrl/go_back
The topic accepts a single Float32 type parameter which is the requested distance in meters. Publishing a value to this topic will cause the robot move backwards by the requested distance.
Example: rostopic pub /base_cntrl/go_back std_msgs/Float32 0.1
## /base_cntrl/go_fwd
The topic accepts a single Float32 type parameter which is the requested distance in meters. Publishing a value to this topic will cause the robot move forward by the requested distance.
Example: rostopic pub /base_cntrl/go_fwd std_msgs/Float32 0.1
## /base_cntrl/go_left
The topic accepts a single Float32 type parameter which is the requested distance in meters. Publishing a value to this topic will cause the robot move left by the requested distance.
Example: rostopic pub /base_cntrl/go_left std_msgs/Float32 0.1
## /base_cntrl/go_right
The topic accepts a single Float32 type parameter which is the requested distance in meters. Publishing a value to this topic will cause the robot move right by the requested distance.
Example: rostopic pub /base_cntrl/go_right std_msgs/Float32 0.1
## /base_cntrl/go_to_pose
The topic accepts a single Pose type parameter which is the requested destination pose for the robot. Publishing a value to this topic will cause the robot move to the requested destination pose.
Example: rostopic pub -1 /base_cntrl/go_to_pose geometry_msgs/Pose '{position: {x: -1.0, y: -2.0, z: 0.0}, orientation: {w: 1.0}}'
## /base_cntrl/scout_to_pose
The topic accepts a single Pose type parameter which is the requested destination pose for the robot to go to for scouting purposes. Publishing a value to this topic will cause the robot move to the requested destination pose and then spin a full circle.
Example: rostopic pub -1 /base_cntrl/scout_to_pose geometry_msgs/Pose '{position: {x: -1.0, y: -2.0, z: 0.0}, orientation: {w: 1.0}}'
## /base_cntrl/in_cmd
The topic accepts a single String type parameter which is the required command for the robot. The robot will react to the following commands:
- fwd
  - Causes the robot to move forward by 1m.
- back
  - Causes the robot to move backwards by 1m.
- right
  - Causes the robot to move right by 1m.
- left
  - Causes the robot to move left by 1m.
- spin
  - Causes the robot to spin in place by 360 degrees.
- shelf<x>
  - Where <x> is a number of the desired shelf, this command causes the robot to navigate to the requested shelf and position itself with a defined offset in front of it.
  - <x> must be an integer in the range of [1..8]
- bin
  - sending “bin” will navigate the robot to a position just in front of the bin.
- scout
  - sending “scout” will navigate the robot to a position more or less in the middle of the map and then the robot will spin a full circle.
- get_cost_of_travel
  - Publishes a 1-dimensional Float32MultiArray message to /base_cntrl/cost_list. The array contains path costs to each of the 8 shelves from the current position of the robot. The path costs are returned in order for the shelves starting at shelf 1.
Example: rostopic pub /base_cntrl/in_cmd std_msgs/String "fwd"
## /base_cntrl/rotate_deg
The topic accepts a single Int16 type parameter, which is the required rotation of the robot in degrees. The value can be either positive or negative. Positive value causes the robot to rotate clock-wise while negative value provides counter-clock-wise rotation.
Example: rostopic pub /base_cntrl/rotate_deg std_msgs/Int16 '{data: -25}'
## /base_cntrl/path_cost_qry
The topic accepts a single Pose which is any reachable point on the map. Publishing a Pose to this toping will resutl in the node Publishing the calculated cost of travel on /base_cntrl/path_cost topic, i.e. the estimated distance to travel to that location.
Example: rostopic pub /base_cntrl/path_cost_qry geometry_msgs/Pose ‘{position: {x: -1.0, y: -2.0, z: 0.0}, orientation: {w: 1.0}}’

# Output Description
# /base_cntrl/path_cost
The topic publlishes a single Float32 value representing the cost of travel from the robot’s current position to the Pose value that was published to the /base_cntrl/path_cost_qry topic.
# /base_cntrl/out_result
This topic publishes a single String value representing the status of the base_controller node.
- If base have completed move forward on command ‘fwd’ out_resutl will publish ‘OK FWD’
- If base have completed move backwards on command ‘back’ out_resutl will publish ‘OK BACK’
- If base have completed move right on command ‘right’ out_resutl will publish ‘OK RIGHT’
- If base have completed move left on command ‘left’ out_resutl will publish ‘OK LEFT’
- If base have completed move spin on command ‘spin’ out_resutl will publish ‘OK SPIN’
- If robot is directed to travel to a specified pose, then /base_cntrl/go_to_pose will request out_result to publish
  - ‘OK MOVE’ if the robot achieves the desired pose
  - ‘BAD MOVE’ if the move can’t be achieved
  - ‘TIMEOUT’ if the robot cant achieve the desired pose in the allocated time.
- If robot is directed to scout- either to a specified pose or to the built in pose in the middle of the map, then out_result will publish one of the following:
  - ‘completed scouting’ if the robot successfully completes the scouting.
  - ‘BAD scouting’ if the scouting failed.
# /base_cntrl/cost_list
This topic will publish a Float32MultiArray, a standard ROS array message type, with a list of cost of travel to each shelf from the current pose of the robot.